M40/R11 Above ground foul drainage systems

315 FLOOR DRAINS

-	Manufacturer: Schlüter-Systems Ltd, Units 3-6   Bardon 22, Beveridge Lane, Coalville, Leics. LE67 1TE. Tel: 01530 813396, Fax: 01530 813376.  E-mail: technical@schluter.co.uk or sales@schluter.co.uk. Web: www.schluter.co.uk

-	Product reference: Schlüter®-KERDI-LINE G3 is a component linear drainage system for floor level showers with a 50mm water seal and a minimum flow rate of 0.4 l/s (single outlet). The system consists of a stainless steel channel, with channel support and a choice of grate and frame options. Available with a horizontal outlet and is supplied with an easily maintained odour trap for internal applications. Install in line with manufacturer’s recommendations, refer to Schlüter®-Systems Technical Data Schlüter®-KERDI-LINE-G3.

The system can be combined with the Schlüter®-KERDI-SHOWER-L, which is a pressure resistant polystyrene sloped board system.

- Floor finish: Suitable for use with tile or stone coverings.

- Body type: - -sTwo part channel and drain casing.

  - Material: V4A Stainless steel (Material no. 1.4404) channel with ABS drain casing and odour trap.

  - Outlet: Offset left or right (Centre of offset 200 mm from end of channel flange. Outlet can be front or rear facing.

- Technical specifications:

  - Drain height = 78 mm

  - 40 mm solvent weld horizontal outlet

  - Pre-applied Schlüter-KERDI waterproofing collar.

  - Suitable for use in perimeter or intermediate floor locations.

  - Odour trap accessible and cleanable from above.

  - Odour trap shutter lock gate clamp for watertight seal.

  - Load rating class = K3

- Compliance information:

  - Tested in accordance with BS EN 1253, BS EN 274 and Building Regulations Approved Document H.

- Accessories:

  - Choice of grate options: A, B, DG3, Floral, Curve and Pure, refer to Schlüter-Systems brochure.

  - Schlüter-KERDI-COLL sealant adhesive to adhere waterproof collar to Schlüter-Systems waterproofing membranes.